## Slide 1: CS 207 PROJECT
FIRE EXTINGUSHING SYSTEM
TOMESH TREVOR

## Slide 2: CREATED BY
VIRAJ PATEL
PREM PATEL
HARSH PATEL

## Slide 3
FIRE EXTINGUSHING SYSTEM

## Slide 4
LIST OF MATERIAL REQUIERD TO BUILT THE CIRCUIT
FLAME SENSOR
Flame Sensor is used to detect the flame
Initial reading is 1(high) but when the flame gets
Detected the reading will 0(low).

## Slide 5
LIST OF MATERIAL REQUIERD TO BUILT THE CIRCUIT
LED
Light Emitting Diode

## Slide 6
LIST OF MATERIAL REQUIERD TO BUILT THE CIRCUIT
Jumper wires

## Slide 7
LIST OF MATERIAL REQUIERD TO BUILT THE CIRCUIT
Buzzer
A buzzer or beeper is an audio signalling device
speaker

## Slide 8
LIST OF MATERIAL REQUIERD TO BUILT THE CIRCUIT
Transister
A transistor is a semiconductor device used to amplify or switch electronic signals and electrical power.

## Slide 9
LIST OF MATERIAL REQUIERD TO BUILT THE CIRCUIT
Register
Register is used to resist the flow of current

## Slide 10
LIST OF MATERIAL REQUIERD TO BUILT THE CIRCUIT
Diode
The function of a diode is to allow an
electric current to pass in one direction

## Slide 11
LIST OF MATERIAL REQUIERD TO BUILT THE CIRCUIT
Mini submersible pump
Mini water pump 3 to 5 volts

## Slide 12
LIST OF MATERIAL REQUIERD TO BUILT THE CIRCUIT
Pipe to connect pump

## Slide 13
LIST OF MATERIAL REQUIERD TO BUILT THE CIRCUIT
Wi-Fi module ( NodMCU )
The ESP8266 WiFi Module is a self contained SOC with
integrated TCP/IP protocol stack that can give any
microcontroller access to your WiFi network.
Used to send the notification.

## Slide 14
Circuit building

## Slide 15
Firstly, connect the Arduino with the breadboard
5 volts with (+)
Ground with (-)
Step 1

## Slide 16
Connect the flame sensor
VCC with (+)
GND with (-)
D0 with (pin 11)
Step 2

## Slide 17
Buzzer is connected with the pin 12
Other to ground
Step 3

## Slide 18
Now the green LED are connected to pin 5
And red LED are connected to pin 6
Step 4

## Slide 19
Now transistor act as switch
Step 5

## Slide 20
Now transister act as switch and resister is connected with base of transister
Step 6

## Slide 21
Now transister act as switch and resister is connected with base of transister
Diode is connected to one end of transister
Step 7

## Slide 22
The end of resister of connected to pin 9 and the (+) diode is with ground
And the one remaining end is with + 5 volts
Step 8

## Slide 23
Mini submersible pump is connected in parallel connection to diode
Step 9

## Slide 24
Coming to connection of Wi-Fi module
Step 10

## Slide 25
Coming to connection of Wi-Fi module
VIN is connected with +5 volts
GND is with ground
Step 11

## Slide 26
Coming to connection of Wi-Fi module
VIN is connected with +5 volts
GND is with ground
D0 pin of flame sensor is connected to D0 pin of Wi-Fi module
Step 12

## Slide 27
Ready for Code ?
HERE WE GO….

## Slide 28: Thank you